## Slide 1: NELoRa Towards Ultra-low SNR LoRa Communication with Neural-enhanced Demodulation
1
Chenning Li1, Hanqing Guo1, Shuai Tong2, Xiao Zeng1, Zhichao Cao1, Mi Zhang1, Qiben Yan1, Li Xiao1, Jiliang Wang2, Yunhao Liu2
1 Michigan State University 2 Tsinghua University
November 15 @ ACM SenSys’21
Notes: A neural-enhanced demodulation for lora communication

## Slide 2: Low-power Wide-area Networks
2
Imaging a world where every single object is connected to the Internet
Notes: Recent years have witnessed the emergence of Low-Power Wide- Area Networks (LPWANs) as a promising mechanism to connect billions of IoT devices. LoRa, SIGFOX, and NB-IoT are the three commercialized wireless technologies that facilitate the establishment of LPWANs.

## Slide 3: IoT Connectivity via LoRa
Gateway
IoT
Sensors
3
PHY Layer: Chirp Spread Spectrum (CSS) Modulation
Long Range
Low Power
Notes: Among them, LoRa achieves the long-range and low-power communication between sensor nodes and gateways。
They key point is to modulate data using Chirp Spread Spectrum (CSS) in the physical Layer of LoRa.
From the sensor nodes to the LoRa gateway, CSS first defines a base up-chirp whose frequency increases linearly. Then it can encode data bits into the shifted initial frequency, as shown in the read line.
In this way, at the gateway side, it can adopt the Dechirp processing for decoding. And it first multiplies the chirp signal with the base down-chirp, the green line, and then applies the FFT on the dechirped signal. Therefore it can focus the chirp energy into the shifted frequency on the spectrum and decode the data bits by detecting the energy peak.

## Slide 4: IoT Connectivity via LoRa
4
(a) SNR = 0
(b) SNR = -10
(c) SNR = -30
Energy Peak Detection
Distorted Energy Peak
Overwhelmed Energy Peak
Time (ms)
Time (ms)
Time (ms)
Long Range
Low Power
Notes: In terms of the long-range and low-power communication, LoRa can suppress the energy of noise by focusing the spectral energy on the spectrum, which allows sensor nodes to send data to gateways several or even tens of miles away.
However, as the SNR gets lower and lower, the energy peak can be distorted or even overwhelmed by the noise energy, resulting the decoding failure.

## Slide 5: IoT Connectivity via LoRa
5
Gateway
IoT
Sensors
Weak Signal Decoding
SNR Threshold of the standard Dechirp processing
Communication Range & Battey Life
Notes: From the sensor nodes to the LoRa gateway, we plot the chirp symbol decoding accuracy with different SNR conditions, under different configurations of LoRa, including SF and BW.
As we can see, the standard LoRa demodulation method, dechirp, determines an SNR threshold under which chirp symbols cannot be decoded reliably.
Generally, a larger SF enables a lower SNR threshold, which results in a longer communication range and larger energy consumption under the same BW.
Given the relationship between the SNR threshold and the communication range, the weak signal decoding has been a hot research topic in our fields.

## Slide 6: SoTAs: Weak Signal Decoding
6
SNR
Gateway
Temporal SNR of a LoRa link
Time
Observed SNR:
SNR Threshold:
SNR Gains
SoTAs
Multiple LoRa Nodes / Gateways
Notes: For example, given the observed SNR of chirp signals and the threshold of the Dechirp processing, to avoid the Dechirp failure, most existing works aim to improve the SNR of observed signals over a weak LoRa link, as the blue curve depicted in this figure.
Such SNR gains are obtained by leveraging information collected from multiple LoRa nodes or gateways. Although these approaches have achieved impressive SNR gains, such gains are obtained costly if the LoRa nodes and gateways are not densely deployed.

## Slide 7: SoTAs: Multi-pair Transceivers
1
2-8
2-6
4-6
7
Charm
IPSN ’18
OPR
MobiSys ’20
Chime
NSDI ’20
Choir
SIGCOMM’17
IoT Sensors
Gateway
SNR
Gains
36
1
1
1
N/A
1-3dB
1.5-2.5dB
2.4-3.4dB
SNR
Gateway
Temporal SNR of a LoRa link
Time
SNR Gains
SoTAs
Observed SNR:
SNR Threshold:
Notes: For instance, Choir leverages up to 36 co-located LoRa nodes to boost the received signal strength; Charm utilizes the spatial diversity of 2 to 8 gateways to decode weak chirp symbols through the coherently decoding processing.

## Slide 8: Problem: Weak Signal Decoding
SoTAs
8
SNR
Gateway
Temporal SNR of a LoRa link
Time
SNR Gains
SNR Gains
Observed SNR:
SNR Threshold:
Notes: All existing solutions inspires us to think about this question, can we optimize the weak signal decoding by decreasing the SNR threshold directly?

## Slide 9
9
SNR
Gateway
Temporal SNR of a LoRa link
Time
SNR Gains
SNR Gains
Motivation: Weak Signal Decoding
NELoRa: neural-enhanced Demodulator
Neural-enhanced Decoder
Extra SNR Gains
Single Pair of LoRa Transceiver
Orthogonal to existing works
SoTAs
Observed SNR:
SNR Threshold:
Observations
System Design
Challenges
Notes: This motivates our work, NELoRa, a data-driven neural-enhanced demodulator.
It aims to capture extra SNR gains by decreasing the SNR threshold of the Dechirp directly.
Besides, it only relies on the single pair of LoRa transceiver and is orthogonal to all existing works.

## Slide 10: Observation-1: Unique Pattern
10
(a) “0x41” - “0x40”
(b) “0x43” - “0x40”
(c) “0x45” - “0x40”
Amplitude
Phase
Time (ms)
Time (ms)
Time (ms)
Takeaway-1: the spectrogram pattern makes it a unique feature
Notes: The idea of applying deep learning stems from our three observations.
First, the chirp itself. As a neural-enhanced decoder, NELoRa takes as input the 2-dimensional spectrogram of chirp symbols, including its amplitude and phase information.
Shown in this figure, we first collect four SF7 chirp symbols. They represent four different but very close data bits.
To illustrate their signal difference more clearly, we plot their spectrogram on the difference of amplitude and phase.
Although the encoded initial frequencies among the four chirps are close, we can clearly observe the unique energy peak distributions from the difference spectrogram. Additionally, we can see peaks (e.g., bright areas) and valleys (e.g., dark areas) alternatively appear in both amplitude and phase spectrograms. Specifically, the patterns observed by amplitude and phase are correlated, but different chirp symbols exhibit diverse patterns. Hence, such a spectrogram pattern is a unique feature dimension to distinguish different chirp symbols.

## Slide 11: Observation-2: 2D Robust Pattern
11
Standard Dechirp
Neural-enhanced Decoder
vs.
Takeaway-2: NELoRa can still recognize it even with partial energy peaks
Notes: The second observation is about the robustness of our 2D spectrogram.
As we know, in the standard Dechirp processing, it detects the 1-dimensional energy peak on the spectrum.
However, NELoRa takes as input the 2-d spectrogram, which is noise-resilient. Specifically, the energy peak distribution on the amplitude spectrogram exhibits a linear pattern. And even facing severe polluted noises, we can still observe parts of energy peaks, which can be potentially learned and recognized by our neural-enhanced decoder.

## Slide 12: Observation-3: Finite Feature Space
12
(a) Across Period
(b) Across Node
(c) Across Environment
SF=7: 128 Different Codes
Takeaway-3: the finite coding space of LoRa for data-driven NELoRa
Notes: The third observations is the finite feature space of LoRa chirp symbols. Since we know LoRa can only encode a fixed size of data bits under certain configurations. For example, for SF=7, it is 2^7=128 codes.
Thus, such a finite feature space can fully exploit the learning ability DNN. Moreover, the finite feature space is robust across different environments. For example, given chirps from different periods, nodes and environments, our trained DNN can always recognize the encoded chirp spectrogram due to its fixed pattern corresponding to. Its encoded data.

## Slide 13: System Design
13
Radio
Front End
PHY Samples
Raw Signals
Preamble
Detection
Chirp
Enhance
Packet
Identification
DNN Input Generation
Offset Recovery
Symbol Generation
Spec-based
Decoder
Symbol
Transform
Mask-enabled
Filter
DNN-based Demodulation
Neural-enhanced Demodulation
LoRa
Packet
LoRa Symbols
1 Packet
Notes: Given our three observations, we design the system framework of NELoRa by incorporating the chirp knowledge and deep learning.
Upon receiving the raw signal from the sensor nodes, NELoRa first adopts signal processing for chirp symbol generation, including packet identification and offset recovery.
Then it feeds the offset-free chirp symbols into our Neural-enhanced Demodulation, covering the spectrogram generation and DNN-based demodulation.
Finally, it outputs the decoded data bits for each LoRa packets.

## Slide 14
14
Add up constructively
Add up destructively
Challenge-1: Symbol Generation
Notes: Before we do the chirp symbol demodulation, the first challenge is how to get the chirp symbols.
Given the preamble of a LoRa packet, say 8 base upchirps in a row, we propose to accumulate the energy of all eight base upchirps on the spectrum thus it can detect the packet under extremely low SNR conditions, which cannot become the bottleneck of our following DNN demodulations.
However, accumulating the 8 base upchirps is non-trivial due to the random initial phase of each base upchirp, resulting in the destructive accumulation on the spectrum.
To achieve the constructive accumulation of those base upchirps, we design a phase searching algorithm for accurately compensating the phase offsets over multiple base upchirps. It cannot only detect the preambles reliably but also compute the offset of the whole packet accurately. After this, we can divide the whole packets into a series of offset-free symbols.

## Slide 15: Challenge-2: Noise & Interference
15
Signal Processing
Filter
Neural-enhanced Filter
vs.
(a) GT Spectrogram
(b) Raw Spectrogram
(c) Masked Spectrogram
SPWVD Mask
Time (ms)
Time (ms)
Time (ms)
DNN Mask
Time (ms)
Time (ms)
Time (ms)
Notes: The second challenge is to deal with the severe noise under low SNR conditions. Since you cannot expect the DNN to recognize the spectrogram pattern directly.
At the beginning, we tried the signal-processing based filter for noise reduction. It aims to extract the primary components of the chirp signals. However, it can only remove noise under a relatively higher SNR, around -10--15dB.
In contrast, we design a mask-based DNN filter, which is a data-driven filter and can derive the clean chirp symbols even under low SNRs such as -20dB.

## Slide 16
Mask-enabled DNN Filter
16
ZeroPad
Conv2d
ReLu
Pooling
Spectrogram-based DNN Decoder
Dense
ReLU
Dropout
SoftMax
Dense
Decoded
Data
GT Data
LSTM
ReLU
Dense
ReLU
Sigmoid
Dense
ZeroPad
Conv2d
BatchNorm
ReLU
Blks
…
Masked Spectrogram
GT Spectrogram
*
Mask
Operation
Challenge-3: Network Design
Dual-channel Spectrogram
(b) 8-channel Output from 8-block CNN
Distorted Energy Peak Distribution
(c) LSTM & Dense1
(a) Input Spec.
Time (ms)
(d) Dense2 / Mask
Time (ms)
(e) Masked Spec.
Time (ms)
*
Notes: The last challenge is the whole DNN design of our neural-enhanced demodulation.
Given the raw spectrogram with amplitude and phase information, we show our deep neural network design with the intermediate results. As mentioned before, the first part is a mask-based DNN filter. As we can see, although the input spectrogram is noisy and cannot be distinguished by human eyes, our DNN network can gradually recognizes the linearly increasing pattern for chirp spectrogram. It outputs a mask and we need to multiply it with the raw spectrogram to reduce the noise.
Upon receiving the clean chirp spectrogram, we design another spectrogram-based DNN decoder, which can exploit the finite coding space of LoRa symbols and output the correct decoded data bits.

## Slide 17: Implementation
17
Metric:
  Symbol Error Rate (SER)
  SNR Gains (SER=10%)
  Battery Life Gain (BLG)
Baseline:
  Standard Dechirp Processing
Notes: We start our implementation and evaluation from this page, including the indoor platform in the building and an outdoor experiment at the campus.
We adopt the commercial LoRa sensor nodes since there is no modification on the sensor side and we use USRP as the gateway.
In terms of evaluation metrics, we care about the symbol error rate of LoRa under different SNR conditions, the SNR gains for SNR threshold when the SER equals to 10%, and the corresponding battery life gains.
All these gains are computed based on our baseline, the standard Dechirp processing.

## Slide 18: Evaluation： Indoor Performance
18
  Q1 - How much does NELoRa improve the demodulation performance than Dechirp under various LoRa configurations?
Notes:   The first question, How much does NELoRa improve the demodulation performance than dechirp under various LoRa configurations?
  We first show the SER and corresponding SNR gains in this page. As you can see, NELoRa outperforms the baseline for all testing configurations. For different SFs, the SNR gain is ranging from 1.84 dB to 2.35 dB. Besides, the SNR threshold of NELoRa at an SF can almost catch up with dechirp at a higher SF. For example, the SNR threshold of NELoRa at SF=7 is close to dechirp’s at SF=8.
  We further evaluate the battery life for NELoRa and the baseline, we can see all the green lines for NELoRa are higher than the red ones, resulting a consistent BLG for different SNR levels and LoRa configurations

## Slide 19: Evaluation： Robustness Analysis
19
  Q2 - How effective is each key technique incorporated in the design of NELoRa?
  Q3 - Is NELoRa robust to different environments for low-cost deployment?
Notes:   Next, we answer these two questions. How effective is each key technique incorporated in the design of NELoRa? Shown in this figure, NELoRa suffers by removing the mask-based filter or spectrogram-based decoder. An interesting thing is that we cannot incorporate DNN filter with the Dechirp, which underperforms in comparison with our DNN decoder.
  Further, we evaluate the robustness of NELoRa, in which we apply our trained DNN model on new data from different periods, nodes and environments directly, without model retraining. This SER-SNR figure shows that NELoRa outperforms the baseline consistently due to the finite feature space of LoRa chirp symsbols.

## Slide 20: Evaluation： Outdoor Performance
20
  Q4. What is the performance of NELoRa in outdoor environment?
Notes:   The last question is about the outdoor performance of NELoRa. We first collect the LoRa packets from 6 positions at the campus and run our end-to-end system from the packet detection to the decoded data bits.
  As we can see, compared with the baseline, the original NELoRa decreases SER of the Dechirp for all six positions
  Besides, we also re-trained our DNN model, which achieves a little better performance than the original one by capturing more unseen noise patterns. This demonstrates that we can further improve NELoRa by updating in an online and distributed manner as more packets are collected across multiple gateways.

## Slide 21: Conclusions
21
The datasets and source codes are available at https://github.com/hanqingguo/NELoRa-Sensys
SNR Threshold of
Demodulation
Communication Range
&
Battey Lifetime
To the best of our knowledge, NELoRa represents the first neural-enhanced LoRa demodulation method with the minimum deployment cost.
Notes: In this paper, we present the design, implementation, and evaluation of NELoRa, a neural-enhanced LoRa demodulation system that breaks the SNR threshold of the standard dechirp approach. The SNR gains enable longer communication distance and battery lifetime in LoRa.
Of course, NELoRa has some limitations as the future work.
First, the maximum SF we evaluated is 10 and a commodity LoRa node can support two larger SFs, namely 11 and 12. With the increasing SF, the chirp symbol length and types exponentially increase. As a result, we must use much more computation to train the DNN model. According to the consistent SNR gains observed when SF increases from 7 to 10, similar SNR gains can be expected when SF is 11 or 12 as long as the DNN model is trainable. we have to optimize the structure of our DNN model to reduce its model complexity and converge time.
Second, currently, NELoRa takes as input the spectrogram of chirp symbols and is incorporated with our packet detection algorithms. However, existing works, such as deepsense, has verified the feasibility of deep learning on carrier sense for efficient channel access. Thus, we expect a holistic neural-enhanced demodulation method in the further.
Third, given widely deployed LoRa nodes, gateways and massive collected data, a promising optimization is to update NELoRa in an online manner, such as the federated learning.